## Slide 1: Mathematica – Applications at Cochlear
Peter Bradley, PhD, Director of Advanced Wireless Technology
5-Jun-25

## Slide 2: What is a Cochlear Implant ?

## Slide 3: Cochlear at a glance
Notes: FY22

## Slide 4: Technical Analysis Tools
Stage | Characterization Test Analysis, Design Analysis, Debug | Verification
Requirements | Free flowing analysis, Self-documenting Flexibility, Ease of use Visualisation (Ideally Dynamic) Statistical Capability Curve fitting and Modeling | Software Robustness, Rigorous testing Self-documenting
Tools | Mathematica, Matlab, Python(+Jupyter), R, Excel | Python commonly used (other possibilities as well)

## Slide 5: Reliability Analysis

## Slide 6: Cosmic Radiation Interaction - Sequence of Events
Primary Cosmic Rays (92% protons, 6% alpha, rest heavy ions)
Secondary Cosmic Ray flux Interaction with atmosphere - N and O2 - gives series of cascade reactions. Resultant spectrum at sea-level is shown below.
Single Event Upsets (Bit Flips in Medical Implants) SRAM memory vulnerable
Postulated by Enrico Fermi in 1949, Feb. 14, 2013 NASA's Fermi Telescope Proves Supernova Remnants Produce Cosmic Rays (Nasa News Link)
High Energy Cosmic Rays are born in magnetic field generated by shock wave of Supernova explosions

## Slide 7: Example 1: Reliability Analysis – Cosmic Radiation on Implants
Highlights
Modelling Worldwide Cosmic Radiation Neutron Flux
Important reliability issue in medical implants (single event memory upsets)
Very difficult with any other tool since complex data sets (elevation, implant distribution world wide, geomagnetic position, neutron flux spectra from cosmic rays). Mathematica has in built connectivity to datasets.
Then capable of complex integration over this data set.
Impossible to do with Matlab

## Slide 8: Radiation Environment Model Using Mathematica
Soft Error Rate Model for Implants
Relative Geographic Distribution of implanted Cardiac Devices
(NOTE: Countries which are not shaded have not been included in the analysis yet)
World Elevation
Geomagnetic Rigidity – influence of Mag Field (interpolation of data presented in JESD89A originally from Shea and Smart)
Combined global distribution of implants with neutron flux model.
A key result is that the approximation of NYC is surprisingly accurate (within a few percent for the given model) for medical implanted devices.
Total neutron flux above 10 MeV is 3.6 x 10-3 n/cm2/s (or equivalently 13 /cm2/hr)

## Slide 9: Wireless Analysis

## Slide 10: Example 2: Communications - Magnetic Induction (MI) Link Modelling
Highlights
A fully computable technical document that looks like a Word document (Not possible in Matlab)
Calculations inbuilt and notebook content generated automatically with document template
Dynamic Visualisation
Complex Symbolic computations (Integrations) not possible in R,Matlab or Python.

## Slide 11: Example 2: Communications – MI Link Modelling
Highlights
A fully computable technical document
This computable document contains the following table of contents

## Slide 12: Example 2: Communications – MI Link Modelling
Highlights
A fully computable technical document
Embedded automatic google search (code to search embedded in doc)

## Slide 13: Example 2: Communications – MI Link Modelling
Highlights
A fully computable technical document
Calculations inbuilt and notebook content generated automatically with document template
Dynamic Visualisation
Complex Symbolic computations not possible in R,Matlab or Python.
ALL COMPUTATIONS DERIVED FROM FIRST PRINCIPLES TO MINIMIZE ERRORS (Many papers have errors in equations!!!)

## Slide 14: Example 2: Communications – MI Link Modelling
Highlights
A fully computable technical document
Calculations inbuilt and notebook content generated automatically with document template
Dynamic Visualisation. The dynamic manipulator is embedded and computable in the document so the user can see what happens when parameters vary
Complex Symbolic computations not possible in R, Matlab or Python. (such as these elliptic integrals)

## Slide 15: Example 2: Communications – MI Link Modelling
Highlights
A fully computable technical document
This visualisation was automatically generated by the document.
Click the picture and hit play for the movie
Animation:
Click mouse over plot to show movie controls
This plot shows the variation in power lost in a low frequency link between a transmitter coil and receiver coil as the receiver coil angle varies. Several similar dynamic visualization methods are used in the computable report

## Slide 16: Example 3: Analytical modelling of antenna matching networks
Highlights
Derives equations symbolically
Solves complex circuit equations analytical (linear algebra of kirchoffs loop equations) (not possible with other tools which are all numeric eg SPICE, Matlab etc)
This is proving extremely useful for our Bluetooth RF design !!
Great for any passive circuit analysis

## Slide 17: Example 4: Communications - Bluetooth Throughput Analysis
Highlights
Dynamically visualize packet construction as we change key bluetooth link parameters
Different displays to teach firmware engineers and optimize link throughput and power consumption => Improve battery life
Hyperlinks to link layer information

## Slide 18: Signal Processing and Chip Development

## Slide 19: Example 5: Analytical modelling for Digital Signal Processing
Requirements
Analytical manipulation and analysis for DSP
Uses symbolic solving capability of recursive equations
Example HPF – IIR with time-variant properties adjusted to optimize DC removal very quickly

## Slide 20: Example 6: Dynamic Visualisation of State Machines
Highlights
Novel concept for verification of state machines
Read code (ANY Code C, RTL etc) and create Boolean expressions
Visualize dynamically the operation and logic of the machine
Impossible to do with Matlab

## Slide 21: Key advantages with respect to other tools
Mathematica combines
  Symbolic computation (absolute best tool, symbolic tools in python and matlab are very weak)
  Excellent notebook for self documenting computable documents
    (been developed for 25 years) Much more powerful than Jupyter in Python
  Dynamic visualisation very easy to code (this makes it really suited to test characterization analysis where visualisation is important and flexibility is key)
  Very strong modelling, statistical analysis and equation solving (since it can do symbolic analytical calculations)
  The examples will show many instances some recently developed and others from my experience that showcase these features especially when combined.
  Competing options don’t adequately combine these capabilities
  It is an excellent tool to supplement others in an Engineers Toolkit.